## Slide 1: Chapter 5: Network Layer: Control Plane
chapter goals: understand principles behind network control plane
traditional routing algorithms
SDN controllers
Internet Control Message Protocol
network management
and their instantiation, implementation in the Internet:
OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP

## Slide 2
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 3: Network-layer functions
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination

## Slide 4
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 5
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 6
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 7: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 8: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 9: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 10: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 11
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 12: A link-state routing algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 13: Dijsktra’s algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 14
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Dijkstra’s algorithm: example
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct shortest path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 15: Dijkstra’s algorithm: another example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 16: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 17: Dijkstra’s algorithm, discussion
algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
oscillations possible:
e.g., support link cost equals amount of carried traffic:
A
D
C
B
1
1+e
e
0
e
1
1
0
0
initially
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
A
D
C
B
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
A
D
C
B
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1

## Slide 18
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 19: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 20: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum is next
hop in shortest path, used in forwarding table
B-F equation says:

## Slide 21: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 22: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 23: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 24
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 25
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 26: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 27: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?

## Slide 28
Distance Vector: link cost increases
x
z
1
4
50
y
60
x y z
y
x
z
4 0 1
0
4
5
5
1
0
from
cost to
x y z
y
x
z
6
from
cost to
node y table
node z table
node x table
Dy(x) = min{c(y,x) + Dx(x), c(y,z) + Dz(x)} = min{60+0 , 1+5} = 6
1
0
x y z
z
y
x
5 1 0
4
0
1
0
4
5
from
cost to
x y z
x
y
z
0 4 5
4
0
1
5
1
0
from
cost to
x y z
z
y
x
7 1 0
from
cost to
Dz(x) = min{c(z,y) + Dy(x), c(z,x) + Dx(x)} = min{1+6, 50+0} = 7
when y detects

## Slide 29
Distance Vector: link cost increases
x
z
1
4
50
y
60
x y z
y
x
z
4 0 1
0
4
5
5
1
0
from
cost to
x y z
y
x
z
6
from
cost to
node y table
node z table
node x table
1
0
x y z
z
y
x
5 1 0
4
0
1
0
4
5
from
cost to
x y z
x
y
z
0 4 5
4
0
1
5
1
0
from
cost to
x y z
z
y
x
7 1 0
from
cost to
Dz(x) = min{c(z,y) + Dy(x), c(z,x) + Dx(x)} = min{1+8, 50+0} = 9
x y z
y
x
z
8
from
cost to
1
0
Dy(x) = min{c(y,x) + Dx(x), c(y,z) + Dz(x)} = min{60+0 , 1+7} = 8
x y z
z
y
x
9 1 0
from
cost to
when y detects

## Slide 30: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 31
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 32: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 33: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 34: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 35: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 36: Intra-AS Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First (IS-IS protocol essentially same as OSPF)
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary for decades, until 2016)

## Slide 37: OSPF (Open Shortest Path First)
“open”: publicly available
uses link-state algorithm
  link state packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
router floods OSPF link-state advertisements to all other routers in entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
  link state: for each attached link
IS-IS routing protocol: nearly identical to OSPF

## Slide 38: OSPF “advanced” features
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set low for best effort ToS; high for real-time ToS)
integrated uni- and multi-cast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.

## Slide 39: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 40: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’es.

## Slide 41
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 42: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 43: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protools

## Slide 44: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 45
Network Layer
Simplified BGP Operations
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 46
AS Numbers (ASNs)
ASNs are 16 bit values.
64512 through 65535 are “private”
Genuity: 1
MIT: 3
JANET: 786
UC San Diego: 7377
AT&T: 7018, 6341, 5074, …
UUNET: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
…
ASNs represent units of routing policy

## Slide 47
4-47
AS Graphs Can Be Fun
The subgraph showing all ASes that have more than 100 neighbors in full
graph of 11,158 nodes. July 6, 2001. Point of view: AT&T route-server

## Slide 48: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 49: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 50: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 51
Network Layer
4-51
BGP Routing Table Example
Use “whois” queries to associate an ASN with “owner” (for example, http://www.arin.net/whois/arinwhois.html)
7018 = AT&T Worldnet, 701 =Uunet, 3561 = Cable & Wireless, …
show ip bgp
BGP table version is 111849680, local router ID is 203.62.248.4
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
. . .
*>i192.35.25.0 134.159.0.1 50 0 16779 1 701 703 i
*>i192.35.29.0 166.49.251.25 50 0 5727 7018 14541 i
*>i192.35.35.0 134.159.0.1 50 0 16779 1 701 1744 i
*>i192.35.37.0 134.159.0.1 50 0 16779 1 3561 i
*>i192.35.39.0 134.159.0.3 50 0 16779 1 701 80 i
*>i192.35.44.0 166.49.251.25 50 0 5727 7018 1785 i
*>i192.35.48.0 203.62.248.34 55 0 16779 209 7843 225 225 225 225 225 i
*>i192.35.49.0 203.62.248.34 55 0 16779 209 7843 225 225 225 225 225 i
*>i192.35.50.0 203.62.248.34 55 0 16779 3549 714 714 714 i
*>i192.35.51.0/25 203.62.248.34 55 0 16779 3549 14744 14744 14744 14744 14744 14744 14744 14744 i
. . .
Thanks to Geoff Huston. http://www.telstra.net/ops on July 6, 2001

## Slide 52: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 53: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d

## Slide 54: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2

## Slide 55: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 56: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263

## Slide 57
4-57
Attributes are Used to Select Best Routes
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
192.0.2.0/24
pick me!
Given multiple
routes to the same
prefix, a BGP speaker
must pick at most
one best route
(Note: it could reject
them all!)

## Slide 58
58
AS PATH Attribute
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341

## Slide 59: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 60: BGP: achieving policy via advertisements
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 61: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 62
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 63
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 64
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 65
data
plane
control
plane
Recall: logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 66
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming: more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane

## Slide 67: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
* Slide courtesy: N. McKeown

## Slide 68: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control “knobs”: wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 69: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 70: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination based forwarding, and LS, DV routing)
Networking 401
Notes: Note: implicit assumption here: destination based forwarding

## Slide 71
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance

## Slide 72
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 73
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 74
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 75
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 76: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller

## Slide 77: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 78: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 79
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4

## Slide 80
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 81
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services

## Slide 82
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 83
SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling

## Slide 84
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 85: ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 86: Traceroute and ICMP
source sends series of UDP segments to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message include name of router & IP address
when ICMP message arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 87: Chapter 5: summary
we’ve learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF, BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
next stop: link layer!